## Slide 1
Hardware and Software Fundamentals of Intelligent Computing Systems
Notes: 需要涉及的要点：
- 第一课时：Compute Architectures 的逐渐演化：由AI/ML workload 引导，逐渐展示出多种多样的架构，如华为达芬奇、AMD等等
- 第二课时：互联的硬件基础，与CUDA core、Tensor core 的编程。
- 可能还需要涉及的点：课程整体设计（Syllabus、各个模块的内容，根据教学大纲生成了个overview的图）

## Slide 2
Lecture 02: Fundamentals of Heterogeneous Computing Programming Models

## Slide 3
Host, Device, and Interconnect
  host-dev: PCIe, NVLink-C2C
  dev-dev: PCIe, NVLink, (RDMA)
Programming CUDA Cores
Programming Tensor Cores
Outline

## Slide 4
AI Hardware Spectrum: Key Examples（1/2）
Cloud ML
NVIDIA DGX 100
Edge ML
NVIDIA Jetson
AGX Orin
Mobile ML
iPhone
Tiny ML
Arduino Nano 33
BLE Sense
Notes: Janapa Reddi, V. ML Systems Textbook. , from https://www.mlsysbook.ai/contents/core/ml_systems/ml_systems.html

## Slide 5
AI Hardware Spectrum: Key Examples（2/2）
https://www.mlsysbook.ai/contents/core/ml_systems/ml_systems.html
Notes: Janapa Reddi, V. ML Systems Textbook. , from https://www.mlsysbook.ai/contents/core/ml_systems/ml_systems.html

## Slide 6
Two Forms of AI Chips (NVIDIA)
Discrete AI Chip: Standalone accelerators (e.g., DGX A100).
Integrated AI Chip: System-on-Chip/SoC (e.g., DRIVE Thor).
Notes: https://applieddatasystems.com/hpc-solutions-2/gpu-servers/
https://developer.nvidia.com/blog/introducing-nvidia-jetson-thor-the-ultimate-platform-for-physical-ai/

## Slide 7
Hetergeneous Integration of CPU and XPUs
Inter-chip (board-level) integration
  protocols: PCIe, NVLink, etc.
Intra-chip integration
  protocols: one-way or two-way coherency
CPU
“host”
XPU
“device”
CPU
“host”
XPU
“device”

## Slide 8
PCIe Basic Knowledge
Market Adoption (in Aug. 2025)
  Mainstream: PCIe 4.0
  Latest device: PCIe 5.0
  Not yet in production: PCIe 6.0/7.0
PCIe Lanes
  “x” = number of lane pairs (TX/RX)
  e.g. PCIe 5.0, “x1” = 4GB/s, “x16” = 32GB/s
  x4: most NVMe SSD, NIC
  x16: most GPU, FPGA
Notes: pic-1 src: https://www.fibermall.com/blog/pcie-development.htm?srsltid=AfmBOorQpZIXd2vThqYRYSiPnQA0t-vEEgy2qs2bqBwevFxZ18Css9BG
pic-2 src: https://global.icydock.com/resources/icy_tips_367.html

## Slide 9
PCIe Architecture
Notes: pic1: https://e2e.ti.com/support/processors-group/processors/f/processors-forum/465737/pcie-system-architecture
pic2: https://www.corsair.com/us/en/explorer/diy-builder/storage/what-is-pcie-and-how-does-it-work/?srsltid=AfmBOopOClHgxQNRCjM-qE1GfLF5emw_NG9baHGOoHVaTlt9bfUfwAtF

## Slide 10
PCIe Devices
GPU
(Nvidia A100, PCIe 4.0 x16)
NVMe SSD
(Sumsung 970, PCIe 4.0 x4)
FPGA
(AMD V80, PCIe 4.0/5.0 x16)
Network Interface Card, NIC
(Intel E810 10/25 GbE, PCIe 4.0 x4)
WiFi 6E Card
(Intel AX210, PCIe 3.0 x1)
RAID Controller
(Broadcom 9560-16i, PCIe 4.0 x8)

## Slide 11
PCIe Role in AI: GPU-Host Connection
GPU connect to most Host with PCIe (currently 2025.08)
  Host->GPU: Commands (CUDA kernels, OpenCL bin)
  Training data, Model weights...
  GPU->Host: GPU status (kernel completion, CUDA events)
  Computation results (gradients, inference output)...
Traditional Data Transfer
  1st Copy: NVMe SSD -> host Memory [with DMA]
  2nd Copy: host Memory -> GPU Memory
Nvidia GPUDirect Storage (from 2020.06)
  Only 1 Copy: NVMe SSD -> GPU Memory
GPUs to mainboard with PCIe
Notes: https://www.zhihu.com/question/22233341/answer/1889610843068535566
gpu-cpu pic src: https://developer.nvidia.com/gpudirect

## Slide 12
PCIe Role in AI: GPU-GPU Connection
GPU connect each other with PCIe (before 2016 NVlink published)
  Data/Pipeline/Tensor/Expert Parallelism
Traditional Data Transfer
  GPU0 write to host shared memory
  GPU1 read from host shared memory
GPUDirect Peer-to-Peer
  Direct access with Load/Store
  Direct transfer with cudaMemCpy()
Notes: gpudirect: https://developer.download.nvidia.com/devzone/devcenter/cuda/docs/GPUDirect_Technology_Overview.pdf
pic src:
https://developer.nvidia.com/blog/introduction-cuda-aware-mpi/
https://keeneland.gatech.edu/software/gpudirect.html
并行方式 产生大量P2P通信的阶段 典型通信量 对P2P带宽/延迟的敏感度
数据并行 梯度聚合（All-Reduce） 大，但可用Ring/Tree算法分摊到多链路 中等
模型并行/张量并行 每一步前向+反向，层内张量切片之间频繁交换中间结果 持续且密集的小包 极高
流水线并行 阶段边界的前向激活 & 反向梯度 阶段性脉冲式流量 高

## Slide 13
NVLink: GPU Interconnect
NVLink 1.0 first introduced with P100 GPU in 2016
  4 NVLinks, each with 8 channels, 40 GB/s bidirectional bandwidth, 160 GB/s in total
  Faster than PCIe 3.0 x 16 (32 GB/s)
Serial communication based on high-speed differential signaling
  NVLink 1.0, 5 GB/s per channel
Notes: pic: https://en.wikichip.org/wiki/nvidia/nvlink

## Slide 14
NVLink Generations
Updatest: NVLink 5.0 in 2024
 | NVLink 1 | NVLink 2 | NVLink 3 | NVLink 4 | NVLink 5
Year | 2016 | 2018 | 2020 | 2022 | 2024
Lanes per port | X8 | X8 | X4 | X2 | X2
Lane rate (Gbps) | 20 | 25 | 50 | 100 | 200
Modulation | NRZ | NRZ | NRZ | PAM4 | PAM4
Nyquist frequency (Gbaud) | 20 | 25 | 50 | 50 | 100
Bidirectional bandwidth per port (GB/s) | 40 | 50 | 50 | 50 | 100
Applicable GPU | P100 | V100 | A100 | H100 | B100
Ports per GPU | 4 | 6 | 12 | 18 | 18
Bandwidth per GPU (GB/s) | 160 | 300 | 600 | 900 | 900
Notes: pic1: https://mp.weixin.qq.com/s?__biz=MzI1OTExNzkzNw==&mid=2650480852&idx=3&sn=9c1730bc2ba0262937e29a7096a0697d&chksm=f3811d2cccd9dfae64115574577a78a3875cdf8ef926a79ac1b03232dc910508cff4df37533b&scene=27&poc_token=HHU-pGij3SZqHxnt9yGj91eq4cMpN2yXbZjC5abD
pic2: https://www.nvidia.com/zh-tw/data-center/nvlink/

## Slide 15
Heterogeneous Host-Device Interaction
without Unified Memory
with Unified Memory
① malloc
② cudaMalloc
③cudaMemcpy
...
⑥cudaMemcpy
④ cudaLaunchKernel
⑤cudaDeviceSynchronize
Notes: 单击此处添加文本

## Slide 16
Host, Device, and Interconnect
Programming CUDA Cores
Programming Tensor Cores
Outline

## Slide 17
Questions on Heterogeneous Programming
How to compile the “kernel” code?
How do CPU and GPU interact?
How to express parallelism?
How to express synchronization?
How to manage and access data?
How is kernel code executed on GPU?
Misc. topics
  debugging tools
  useful libraries

## Slide 18
(incomplete list of) Concepts on Hetero-Programming
How to compile the “kernel” code?
How do CPU and GPU interact?
How to express parallelism?
How to express synchronization?
How to manage and access data?
How is kernel code executed on GPU?
a “”compiler” (later lectures)
host, device, kernels
threads, blocks, grid
__syncthreads()
xxMalloc(), xxxMemcpy(), global/shared/constant
warp scheduling

## Slide 19
How do CPU and GPU interact?
A Tale of Host and Device
  host ~ CPU; device ~ GPU
  in OpenCL/ROCm, CPUs can also serve as devices
CPU-GPU interface
  x86-NV5090 @ PCIe 5.0: 64 GB/s
  Grace-Hopper NVLink C2C: 900 GB/s
  Grace-Blackwell NVLink C2C: 1.8 TB/s
kernel ≈ a device function interface for the host
xxxMalloc(), xxxMemcpy()

## Slide 20
How do CPU and GPU interact? (host program)
Host program
  Running as part of normal C/C++ application on CPU
  Launch a grid of kernel thread blocks
  Call returns when all threads have terminated

## Slide 21
How do CPU and GPU interact? (kernel program)
Kernel definition
  __global__ denotes a kernel function
  Thread computes its thread id from its position in its block (threadIdx) and its block’s position in the grid (blockIdx)

## Slide 22
How to Express Parallelism?
Thread Hierachy
  Thread
    The smallest unit of execution
    (not the smallest unit of scheduling)
  Thread Block (Block)
    A group of threads
    Cooperate through shared memory and synchronization
    Organized in up to 3-dims
  Grid
    A collection of thread blocks
    Organized in up to 3-dims
    Lauched by CPUs, executed on GPUs

## Slide 23
The Grid: Blocks of Threads in 1D
adapted from UW CSEP 590, Dr. Hari Sadasivan
Threads in grid have access to:
  Their respective block: blockIdx.x (for the “Thread” above: == 4)
  Their respective thread ID in a block: threadIdx.x (for the “Thread” above: == 0)
  Their block's dimension: blockDim.x (for the example above: == 4)
  The number of blocks in the grid: gridDim.x (for the example above: == 8)

## Slide 24
The Grid: Blocks of Threads in 2D
Each color is a block of threads
Each small square is a thread
The concept is the same in 1D and 2D
In 2D each block and thread now has
a two-dimensional index
Threads in grid have access to:
  Their respective block IDs: blockIdx.x, blockIdx.y
  Their respective thread IDs in a block: threadIdx.x, threadIdx.y
adapted from UW CSEP 590, Dr. Hari Sadasivan

## Slide 25
How to Express Synchronizations?
__syncthreads()
xxxDeviceSynchronize()
events
(to be discussed in later lectures)

## Slide 26
How to Manage and Access Data?
CUDA memory model
  Distinct host and device address spaces (when not using unified memory)
  Memory allocation in GPU through cudaMalloc()
  Move data between address spaces through cudaMemcpy()

## Slide 27
How to Manage and Access Data?
CUDA memory model
  Three distinct types of address spaces visible to kernels
  __global__: accessible by all threads
  __device__: distinct from CPU memory
  __shared__: shared by threads in a block

## Slide 28
How is Kernel Code Executed on GPU?
SIMD execution can be combined with pipelining
ALUs all execute the same instruction
Pipelining is used to break instruction into phases
When first instruction completes (4 cycles here), the next instruction is ready to execute
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Add
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
Mul
…
…
Cycle
SIMD Width
(16 in AMD)
(8 in NVIDIA)
AMD: Wavefront
(64 work-items)
NVIDIA: Warp
(32 threads)

## Slide 29
SIMD, SPMD, and SIMT (1/3)
https://www.intel.com/content/www/us/en/developer/articles/technical/accelerating-compute-intensive-workloads-with-intel-avx-512-using-microsoft-visual-studio.html
SIMD is an architecture
  A single sequential instruction stream of SIMD instructions
  For example, a matrix-vector multiplcation using AVX-512:
static float *outx16; static float *avx512Multiply() { for (uint64_t i = 0; i < row; i++) { __m512 sumx16 = _mm512_set1_ps(0.0); for (uint64_t j = 0; j < col; j += 16) { __m512 a = _mm512_loadu_ps(&(t1[i*col + j])); __m512 b = _mm512_loadu_ps(&(t2[j])); sumx16 = _mm512_fmadd_ps(a, b, sumx16); } outx16[i] = _mm512_reduce_add_ps(sumx16); } return outx16; }

## Slide 30
SIMD, SPMD, and SIMT (2/3)
SPMD is a programming paradigm
  “programmers normally write a single program that runs on all processors of an MIMD computer, relying on conditional statements when different processors should execute different sections of code.”
  see Section 6.3 of Computer Organization and Design, Fifth Edition: The Hardware/Software interface by David A. Patterson, John L. Hennessy

## Slide 31
SIMD, SPMD, and SIMT (3/3)
adapted from UW CSEP 590, Dr. Hari Sadasivan
SIMT is both a programming model and an execution model
  Multiple instruction streams of scalar instructions
  Can treat each thread separately
    i.e., can execute each thread independently (on any type of scalar pipeline)
    MIMD processing
  Can group threads into warps flexibly
    i.e., can group threads that are supposed to truly execute the same instruction
    dynamically obtain and maximize benefits of SIMD processing
    For NVIDIA GPUs, warp size = 32; For AMD GPUs, wavefront size = 64
Notes: https://developer.nvidia.com/blog/using-cuda-warp-level-primitives/
NVIDIA GPUs execute warps of 32 parallel threads using SIMT, which enables each thread to access its own registers, to load and store from divergent addresses, and to follow divergent control flow paths.

## Slide 32
SIMT: How to Express the Work of a Thread? (the Single Instruction Stream in SIMT)
A simple embarrassingly parallel loop:
for (int i= 0; i<N; i++)
h_a[i] *= 2.0;
Can be translated into a GPU kernel:
__global__ void myKernel(int N, double *d_a) {
int i = threadldx.x + blockldx.x * blockDim.x;
if (i<N) d_a[i] *= 2.0;
}
adapted from UW CSEP 590, Dr. Hari Sadasivan
A device function that will be launched from the host program is called a kernel & is declared with the __global__ attribute
Kernels should be declared void
All pointers passed to kernels must point to memory on the device
All threads execute the kernel's body “simultaneously”
Each thread uses its unique thread and block IDs to compute a global ID
There could be more than N threads in the grid

## Slide 33
SIMT: How to Express the Thread Structure? (The Grid: Multi-threading in SIMT)
Kernels are launched from the host:
dim3 threads(256,1,1); // 3D dimensions of a block of threads
dim3 blocks((N+256-1)/256,1,1); // 3D dimensions the grid of blocks
myKernel<<<blocks,threads,0,0>>>(N,a);

## Slide 34
Optimizations
Resource-aware optimizations
  resouces: SM, registers, shared memory, memory bandwidth
How? (a incomplete list)
  choose an “optimal” block size, to maximize active warps
    improve the utilization of memory bandwidth →
  after partitioning, map the (task, data) to a suitable thread id
    avoid control divergence
    coalese global memory access
    avoid shared memory bank conflicts
Performance analysis tools

## Slide 35
Coalescing Memory Accesses: Example
  Array X is a pointer to an array of integers (4-bytes each) located at address 0x00001232
  A thread wants to access the data at X[0]
    int tmp = X[0];
0x00001232
X
0
1
2
3
4
5
6
7
0x00001232
0x00001236
0x00001248
.
.
.
.
.
.
.
Notes: This is the start of an example explaining how GPU’s wide memory buses work.

## Slide 36
Coalescing Memory Accesses: Bus Addressing (1/2)
Assume that the GDDR memory bus is 32-bytes (256-bits) wide
The byte-addressable bus must make accesses that are aligned to the bus width, so the bottom 5 bits are masked off
Any access in the range 0x00001220 to 0x0000123F will produce the address 0x00001220
Desired address: | 0x00001232
Bus mask: | 0xFFFFFFE0
Bus access: | 0x00001220

## Slide 37
Coalescing Memory Accesses: Bus Addressing (2/2)
All data in the range 0x00001220 to 0x0000123F is returned on the bus
In this case, 4 bytes are useful and 28 bytes are wasted
?
?
?
0
1
2
3
4
0x00001232
Send an address
Receive data
0x00001220
Memory Controller
Desired element
Notes: The desired element is at 0x00001232 as shown 2 slides back.

## Slide 38
Coalescing Memory Accesses (1/2)
To fully utilize the bus, GPUs combine the accesses of multiple threads into fewer requests when possible
Consider the following kernel code:
Assuming that array X is the same array from the example, the first 16 threads will access addresses 0x00001232 through 0x00001272
If each request was sent out individually, there would be 16 accesses total, with 64 useful bytes of data and 448 wasted bytes
  Notice that each access in the same 32-byte range would return exactly the same data
int tmp = X[threadIdx.x + blockDim.x * blockIdx.x];

## Slide 39
Coalescing Memory Accesses (2/2)
When GPU threads access data in the same 32-byte range, multiple accesses are combined so that each range is only accessed once
  Combining accesses is called coalescing
For this example, only 3 accesses are required
  If the start of the array was 256-bit aligned, only two accesses would be required
?
?
?
0
1
2
3
4
0x00001220
5
6
7
8
9
10
11
12
0x00001240
13
14
15
?
?
?
?
?
0x00001260

## Slide 40
Host, Device, and Interconnect
Programming CUDA Cores
Programming Tensor Cores
Outline

## Slide 41
Tensor Core Evolution
Trending:
  Larger MMA size and arithmetic intensity
  Support for lower precisions and async, vectorized memory copy
Arch | Dtype | TC per SM | TC m,n,k | Sparsity | Mem. Access | Instructions
Volta(SM70) | FP16 | 8 | 4 x 4 x 4 | No | N/A | mma
Turing(SM75) | FP16,INT8,INT4,Binary | 8 | 4 x 4 x 4 | No | ldmatrix | mma,ldmatrix
Ampere(SM80) | FP16,BF16,TF32,FP64,INT8,INT4,Binary | 4 | 8 x 4 x 8 | Yes | async Copy | mma,ldmatrix, mma.sp
Hopper(SM90) | FP16,BF16,TF32,FP64,INT8,Binary | 4 | 8 x 4 x 16 | Yes | TMA | mma,ldmatrix, mma.sp, wgmma

## Slide 42
Tensor Core Evolution

## Slide 43
MMA Overview
Given a matrix, the multiply and accumulate (MMA) instruction computes D = A * B + C:
  A is an M by K matrix
  B is a K by N matrix
  C and D are M by N matrices
We denote the matrix shapes as mMnNkK or MxNxK.
SMEM <-> RF <-> Tensor Core

## Slide 44
The Solution: FlagOS, a Unified AI Software Stack

## Slide 45
https://github.com/flagos-ai
https://space.bilibili.com/3546791834290849
https://www.zhihu.com/people/95-22-20-18/posts
https://flagos.io/Home

## Slide 46
Thanks for your time！