## Slide 1
Hardware and Software Fundamentals of Intelligent Computing Systems

## Slide 2
Lecture 24：Layout and Memory Planning

## Slide 3
GPU Memory Hierarchy
Bandwidth increases 10-100x from left to right 10-100x
Capacity decreases 100-1000x from right to left 100-1000x
The key to layout optimization is maximizing high-speed memory utilization
  Design programs for efficient memory usage, minimizing excessive data movement
  FlashAttention core design philosophy

## Slide 4
GPU Memory Transaction Mechanism
GPU accesses Global Memory not byte-by-byte, but in fixed-size "transactions":
  Each memory transaction transfers 32 bytes or 128 bytes
  Transactions must be aligned to their size boundaries
  A warp（32 threads) are coalesced into as few transactions as possible
  Maximum concurrent transactions are limited，constrained by memory controller queue depth
  Number of transactions × latency = total wait time
Coalesced Access
  When a warp 's 32 threads access addresses meeting the following conditions, they can be coalesced into minimal transactions
  Addresses fall within the same or adjacent cache lines
  Each thread accesses contiguous elements

## Slide 5
GPU Memory Transaction Mechanism
Contiguous access：1 transaction(s) suffice
Strided access：2 transactions
int idx = threadIdx.x 2; // T0→0, T1→2, T2→4, ...
float val = data[idx];
int idx = threadIdx.x; // T0→0, T1→1, T2→2, ...
float val = data[idx]; // Contiguous addresses

## Slide 6
GPU Memory Transaction Mechanism
Random access: worst case 32 transactions
Efficiency Comparison
int idx = index_table[threadIdx.x]; // Random addresses
float val = data[idx];
Stride | Transactions | Bandwidth Utilization
1 | 1 | 100%
2 | 2 | 50%
4 | 4 | 25%
32 | 32 | 3.125%
Random | Up to 32 | ～3.125%

## Slide 7
Matrix Access: Row-Major vs Column-Major
A warp reads one row
A warp reads one column
int col = threadIdx.x; // 0,1,2,...,31
float val = M[row 32 + col];
int row = threadIdx.x; // 0,1,2,...,31
float val = M[row 32 + col];

## Slide 8
GPU Shared Memory
~100x faster than Global Memory ~100 x, but ~1000x smaller in capacity~1000
  Programmers can explicitly control data placement
  Shares space with L1 Cache Cache; ratio is manually configurable
Shared Memory is divided into 32 independent Bank
  Can simultaneously serve 32 requests
  Ideal case: 32 threads simultaneously access 32 different Bank
Efficient utilization of Shared Memory is the core of memory layout planning
  When multiple threads within the same Warp map to the same Bank , serialized access is required

## Slide 9
GPU Shared Memory
Ideal Case vs. Worst Case
Access patterns causing Bank Conflict
  Access with specific stride values
  Access with specific stride value（32）
int row = threadIdx.x; // 0 to 31
float val = smem[row][0]; // All threads access column 0
int idx = threadIdx.x 32;
float val = smem_1d[idx]; // idx = 0, 32, 64, 96, ... All mapped to Bank 0

## Slide 10
Resolving Bank Conflict
Padding
  Increase actual storage size per row, staggering column elements to different Bank
Swizzling
  Dynamically alter address mapping via XOR operations, so the same column in different rows maps to different Bank
  Original: addr = row × stride + col
  Swizzle: addr = row × stride + (col XOR row)
__shared__ float smem[32][32]; Row 0: [B0 ][B1 ][B2 ]...[B31] ← 128 bytes
Row 1: [B0 ][B1 ][B2 ]...[B31] ← 128 bytes, starts at Bank 0
Row 2: [B0 ][B1 ][B2 ]...[B31] Column access: : smem[0][0], smem[1][0], smem[2][0], ...
All in Bank 0 → 32-way conflict
__shared__ float smem[32][33]; // Each row has 1 extra element(s) Row 0: [B0 ][B1 ][B2 ]...[B31][B0 ] ← 132 bytes (33 float)
Row 1: [B1 ][B2 ][B3 ]...[B0 ][B1 ] ← starts at Bank 1
Row 2: [B2 ][B3 ][B4 ]...[B1 ][B2 ] ← starts at Bank 2 Column access: : smem[0][0] → Bank 0
smem[1][0] → Bank 1 ← Different Bank
smem[2][0] → Bank 2 ← Different Bank
No conflict
Accessing column 0:
row 0, col 0 → addr 0 → Bank 0
row 1, col 0 → addr 128 → Bank 0
row 2, col 0 → addr 256 → Bank 0
row 3, col 0 → addr 384 → Bank 0
32-way conflict
Accessing column 0 (col XOR row):
row 0, col 0^0=0 → Bank 0
row 1, col 0^1=1 → Bank 1
row 2, col 0^2=2 → Bank 2
row 3, col 0^3=3 → Bank 3
No conflict

## Slide 11
Triton Automatic Layout Optimization
The compiler automatically generates swizzled access code based on these parameters
  vec: Number of contiguously accessed elements, affects vectorization
  perPhase and maxPhase: Control swizzle period
Triton compiler automatically handles Shared Memory layout optimization
#shared = #triton_gpu.shared<{
  vec = 4, // Vectorization width (accesses 4 elements at once)
  perPhase = 2, // Rows per phase
  maxPhase = 8, // Maximum phase count (for swizzle)
  order = [1, 0], // Memory traversal order
  hasLeadingOffset = false
}
@triton.jit
def kernel(...):
  # Triton automatically selects optimal layout
  a = tl.load(A_ptr + offs) # Global → Register
  # Explicitly using shared memory
  # Triton automatically applies swizzling
  a_shared = tl.trans(a) # Auto-optimized during transpose

## Slide 12
Tensor Layout
Mapping from logical tensor elements to physical storage locations
  Memory arrangement order
  Distribution of elements across hardware units
Common Layout Types
  Row-major，Row-contiguous storage, ，C/C++ default
  Column-major，Column-contiguous storage，Fortran, MATLAB
  Blocked，Block storage, ，GPU parallelism
  Strided，Strided storage，Slicing operations
2x4 matrix: : Row-major:
┌─┬─┬─┬─┐ [0,1,2,3,4,5,6,7]
│0│1│2│3│
├─┼─┼─┼─┤ Column-major
│4│5│6│7│ [0,4,1,5,2,6,3,7]
└─┴─┴─┴─┘

## Slide 13
Triton Layout Encoding
Using MLIR Attribute to represent layouts
  BlockedEncodingAttr: GPU Global memory access pattern
  SharedEncodingAttr: Shared memory access pattern (swizzle)
  NvidiaMmaEncodingAttr: Tensor Core operation layout
  DotOperandEncodingAttr: Matrix multiplication operand layout
Unified Layout Representation
  Represent layouts as mappings from hardware positions (warp, thread, register) to logical indices (m, n)
  Use binary bits for strides, XOR operation composition
#blocked = #triton_gpu.blocked<{
  sizePerThread = [4], // Elements per thread
  threadsPerWarp = [32], // Threads per warp
  warpsPerCTA = [4], // Threads per CTA warp count
  order = [0] // Dimension traversal order
}>

## Slide 14
MMA (Matrix Multiply-Accumulate) Layout
Data arrangement designed for GPU Tensor Core
  Tensor Core computes D = A × B + C
  Fragment size is fixed (e.g., Volta architecture 16*16), conforming to TC hardware requirements
  Each thread holds 8 elements
  Thread 0: A[0,0:2], A[8,0:2], A[0,8:10], A[8,8:10]；Thread 1: A[0,2:4], A[8,2:4], A[0,10:12]；...

## Slide 15
MMA (Matrix Multiply-Accumulate) layout
From Blocked to MMA Layout Conversion
  ldmatrix instruction, loads from shared memory and rearranges to MMA layout
  Read 8×8 matrix fragment from shared memory->Distribute to registers of threads within the warp ->Rearrange to MMA
Triton in TritonMMA Encoding Attribute
Triton Layout Conversion in Triton
#mma = #triton_gpu.nvidia_mma<{
  versionMajor = 2, // MMA version (1=Volta, 2=Ampere, 3=Hopper)
  versionMinor = 0,
  warpsPerCTA = [2, 2], // Warp grid layout
  instrShape = [16, 8, 16] // M × N × K instruction shape
}>
// From blocked layout to mma layout
%0 = triton_gpu.convert_layout %arg :
tensor<128x64xf16, #blocked> -> tensor<128x64xf16, #mma>

## Slide 16
Memory Allocation Strategies
Static Allocation
  Compile-time allocation，0 runtime overhead, predictable fragmentation, low flexibility
  All tensor sizes known at compile time
Dynamic Allocation
  Runtime allocation, with malloc overhead, high flexibility
ML Compiler Strategy
  Compile-time analysis -> determine tensor lifetimes -> compute optimal allocation plan -> generate allocation code
  Use memory pools to support dynamic shapes

## Slide 17
Memory Reuse
Tensors with non-overlapping lifetimes can share memory
  ABC can be reused among each other
  D and ABC cannot be reused
Common Algorithms
  Graph Coloring: Build interference graph, minimize number of colors
  Greedy Algorithm: Sort tensors by size, maximize reuse
ILP Method: Integer Linear Programming for optimal solution
  Minimize: : max(offset[i] + size[i]) for all i
  Constraints: : 1. offset[i] >= 0 (Non-negative offset)
  2. offset[i] + size[i] <= offset[j] (if i, j non-overlapping and i precedes) or offset[j] + size[j] <= offset[i] (if j precedes)
  3. Tensors with overlapping lifetimes must have distinct address spaces
Tensor A: ████████████
Tensor B: ████████████
Tensor C: ██████████
Tensor D: ████████████████████

## Slide 18
Tensor Rematerialization
Image Source: Capuchin: Tensor-based GPU Memory Management for Deep Learning
GPU memory insufficient to store all intermediate tensors
Selectively discard and recompute
  Input->A->B->C->Output
  Do not store A, retain B and C for backward pass
  Recompute during backward pass: A
Optimization Objective: Minimize (computation time + peak memory)
  Runtime dynamic decision-making
  Optimization problem solving
Notes: 单击此处添加文本

## Slide 19
Layout and Memory Planning Optimization Strategies
Layout Conversion
  Defer conversions as late as possible
  Detect and remove redundant conversions
  Merge adjacent conversions
Prefer layouts favorable to dominant operations
  Consider the entire computation graph, not just individual operators
Reduce Conversions
  Unify to the same layout
  Perform conversions at compute-intensive points
Combined with Dead Code Elimination
  Reduce memory allocation: Remove dead variables -> no allocation needed
  Shorten lifetimes: Remove useless operations -> free memory earlier
  Enable more reuse: Shorter lifetimes -> more reuse opportunities

## Slide 20
The Solution: FlagOS, a Unified AI Software Stack

## Slide 21
https://github.com/flagos-ai
https://space.bilibili.com/3546791834290849
https://www.zhihu.com/people/95-22-20-18/posts
https://flagos.io/Home

## Slide 22
Thanks for your time！