## Slide 1: Hardware and Software Fundamentals of Intelligent Computing Systems

## Slide 2: Lecture 32: Communication Topology Optimization

## Slide 3: Implementations of collective communication operators
All-reduce = Reduce-scatter + all-gather
Ring All-reduce
NVIDIA GPU CLOS Topology
HUAWEI NPU Full-mesh Topology
The implementations
highly depends on
the hardware topology

## Slide 4: Topologies in the modern AI systems
GOOGLE TPU Torus Topology
HUAWEI NPU Full-mesh Topology
NVIDIA GPU Clos Topology
Dragonfly Topology

## Slide 5: Take AllReduce as an example
Start from a naive implementation with root rank = 0.
  Data transfer volume: 2 * (N-1) * K
There are three disadvantages
  The bandwidth and computation of Rank 0 become bottleneck.
  There are many idle resources during the allreduce (Rank 1 – N-1).
  Poor scalability and lacks the consideration of topology.
How can we improve it?
  Scatter the data transfer and computation workload to all of the ranks.
Solutions:
  Tree-based, ring-based, halving-doubling, etc.

## Slide 6: Take AllReduce as an example
Tree-based AllReduce Algorithm
  Build a hierarchical relation with the root of tree (Rank 0).
  Stage 1: Bottom-up Reduce
  Stage 2: Top-down Broadcast
0
1
2
3
4
5
6
7
0+1
1
2+3
3
4+5
5
6+7
7
Rank 0
Rank 7
S1 Reduce
0+1+2+3
1
2+3
3
4+5+6+7
5
6+7
7
SUM(0,7)
1
2+3
3
4+5+6+7
5
6+7
7

## Slide 7: Take AllReduce as an example
Tree-based AllReduce Algorithm
  Build a hierarchical relation with the root of tree (Rank 0).
  Stage 1: Bottom-up Reduce
  Stage 2: Top-down Broadcast
1
2
3
4
5
6
7
Rank 0
Rank 7
S2 Broadcast
SUM(0,7)
SUM(0,7)
1
2
3
5
6
7
SUM(0,7)
SUM(0,7)
1
SUM(0,7)
3
5
SUM(0,7)
7
SUM(0,7)
SUM(0,7)
SUM(0,7)
SUM(0,7)
SUM(0,7)
SUM(0,7)
SUM(0,7)
SUM(0,7)
SUM(0,7)

## Slide 8: Take AllReduce as an example
Tree-based AllReduce Algorithm
  Build a hierarchical relation with the root of tree (Rank 0).
  Stage 1: Bottom-up Reduce
  Stage 2: Top-down Broadcast
Advantages
  Parallel data transfer and reduce operations.
  Logarithmic complexity (the naive version has linear complexity).
  It excels with small data sizes because of the low latency.
Disadvantages
  It still has idle computing and bandwidth resources.
Further Opt: Double Binary Tree (NCCL)

## Slide 9: Take AllReduce as an example
Ring-based AllReduce Algorithm
  Stage 1: Iterative Reduce
  Stage 2: Iterative Gather

## Slide 10: Take AllReduce as an example
Ring-based AllReduce Algorithm
  Stage 1: Iterative Reduce with N-1 steps
  Stage 2: Iterative Gather with N-1 steps
Split the data with N partitions

## Slide 11: Take AllReduce as an example
Ring-based AllReduce Algorithm
  Stage 1: Iterative Reduce with N-1 steps
  Stage 2: Iterative Gather with N-1 steps

## Slide 12: Take AllReduce as an example
Ring-based AllReduce Algorithm
  Stage 1: Iterative Reduce with N-1 steps
  Stage 2: Iterative Gather with N-1 steps

## Slide 13: Take AllReduce as an example
Ring-based AllReduce Algorithm
  Stage 1: Iterative Reduce with N-1 steps
  Stage 2: Iterative Gather with N-1 steps

## Slide 14: Take AllReduce as an example
Ring-based AllReduce Algorithm
  Stage 1: Iterative Reduce with N-1 steps
  Stage 2: Iterative Gather with N-1 steps

## Slide 15: Take AllReduce as an example
Ring-based AllReduce Algorithm
  Stage 1: Iterative Reduce with N-1 steps
  Stage 2: Iterative Gather with N-1 steps

## Slide 16: Take AllReduce as an example
Ring-based AllReduce Algorithm
  Stage 1: Iterative Reduce with N-1 steps
  Stage 2: Iterative Gather with N-1 steps
Quantitative Analysis
  Data Transfer Volume: 2 * (N-1) * K / N
  Overall Time: 2 * (N-1) * alpha + 2 * (N-1) * K / N / beta
  Tree-based AllReduce Time : 2 * log(N) * (alpha + K / beta)
  alpha: latency; beta: bandwidth
Advantages: Optimal bandwidth utilization

## Slide 17: Take AllReduce as an example
Ring-based AllReduce Algorithm
  Stage 1: Iterative Reduce with N-1 steps
  Stage 2: Iterative Gather with N-1 steps
Quantitative Analysis
  Data Transfer Volume: 2 * (N-1) * K / N
  Overall Time: 2 * (N-1) * alpha + 2 * (N-1) * K / N / beta
  Tree-based AllReduce Time : 2 * log(N) * (alpha + K / beta)
  alpha: latency; beta: bandwidth
Advantages: Optimal bandwidth utilization

## Slide 18: Take AllReduce as an example
Halving-doubling AllReduce Algorithm
  Stage 1: Recursive halving reduce
  Stage 2: Recursive doubling gather

## Slide 19: Take AllReduce as an example
Comparisons among ring-based, tree-based, and halving-doubling Allreduce algorithms.
Modern CCLs can select an efficient strategy according to the topology and the communication domain.
Algorithm | Steps (Complexity) | Latency | Bandwidth Efficiency | Ideal Data Size
Ring-based | O(N) | High | Optimal | Large Data (> 64MB)
Tree-based | O(log N) | Lowest | Moderate | Small-Medium (< 16MB)
Halving-Doubling | O(log N) | Low | Moderate | Very Small (< 1MB)
Notes: https://zhuanlan.zhihu.com/p/1976385706453652306

## Slide 20: Besides, the protocol designs are also important
Take NCCL as an example.

## Slide 21: Besides, the protocol designs are also important
Take NCCL as an example.
Notes: https://zhuanlan.zhihu.com/p/1976385706453652306

## Slide 22: The Solution: FlagOS, a Unified AI Software Stack

## Slide 23
https://github.com/flagos-ai
https://space.bilibili.com/3546791834290849
https://www.zhihu.com/people/95-22-20-18/posts
https://flagos.io/Home

## Slide 24: Thanks for your time！