## Slide 1: Hardware and Software Fundamentals of Intelligent Computing Systems

## Slide 2: Lecture 43: Extreme Optimization of Heterogeneous Systems

## Slide 3: Microarchitecture of Heterogeneous Systems
Architecture Evolution: From a single SIMT model toward architectures integrating tensor engines, asynchronous memory, and massive on-chip caches.
Ecosystem Differences: Fundamental differences exist in instruction throughput, register file sizes, and memory topologies across different hardware.
Optimization Requirements: Relying on abstract general-purpose compilers often leads to pipeline stalls or idle bandwidth; targeted specialization is essential.

## Slide 4: Typical Domestic GPU Microarchitecture Examples
Moore Threads (Moore Threads): Fifth-generation“Huagang” architecture, supporting next-generation asynchronous programming models and FP4 quantized data format, supporting clusters of over 100,000 cards .
Biren Technology (Biren):BR100 architecture, equipped with 300MB massive on-chip cache and 64GB HBM2E, minimizing global memory access latency to the extreme .

## Slide 5: Case Study:Background and Challenges
Objective
  Taking tle.gpu.local_ptr as an example, introduce how toimplement microarchitecture optimization for specific architectures
  Code Location:https://github.com/flagos-ai/FlagTree/pull/333
Core Challenges
  Generic optimizations cannot reach the low-level details
  Shared memory access bottleneck
  Significant operator performance gaps
    e.g.,moe_align_block_size, topk etc.
  Software stack fragmentation

## Slide 6: Hardware Principles and Memory Access Optimization Fundamentals
Shared Memory Core Characteristics
  Bank Structure: divided into 32 bankss, every 4 bytes spanning across banks; parallel access without conflicts
  Thread Block Visible: the same CTA share it, requiring __syncthreads() for synchronization
  Explicit Management:Programmer//compiler explicitly controls allocation; not a transparent cache
  Domestic Chip Differences:Some domestic GPU 's bank bank width and address mapping differ from NVIDIA
  local_ptr Significance: Verify via local_ptr abstraction, uniformly express shared mem pointer operations
Register
Fastest ~1 cycle
Shared Memory
Very Fast ~5 cycles, thread block shared
L1 Cache / Texture
Fast ~30 cycles
L2 Cache
Moderately Fast ~100 cycles
Global Memory (HBM)
Slow ~400+ cycles
Latency increases from top to bottom ▲

## Slide 7: FlagGems Overview
Triton -written, Cross-Hardware Unified:
  Natively supports CUDA,MLU,XPU,NPU etc. 10+ hardware backends
High-Performance Operators:
  Core training and inference operators including matrix operations, attention mechanisms, normalization, and activation functions
LibEntry Kernel Cache:
  In-house dispatch layer replacing Triton native Autotuner, significantly reducing first-compilation overhead and dispatch dispatch latency
Dual-Mode Deployment:
  Pure Python package (quick validation) and C++ extension (production acceleration) freely switchable;C++ path eliminates Python call frame overhead
Configuration-Driven Tuning:
  LibTuner automatically searches for optimal hyperparameters and persists them as YAML; cold start directly reuses them without re-running benchmark

## Slide 8: FlagTree System Overview
Unified Multi-Chip AI Operator Compiler · Based on Triton & MLIR Ecosystem
Supported Chip Backends (10+ domestic and international mainstream AI chips)
  NVIDIA,Cambricon,Tsingmicro,Huawei Ascend,Moore Threads, etc.
  Multiple Triton version branches (v3.1 ~ v3.5) maintained in parallel; independent CI/CD
Python Frontend
@triton.jit
FlagGems LibEntry
▶
Compiler Middle Layer
MLIR Dialects
Triton-IR / TTGIR
▶
Backend Code Generation
LLVM-IR → PTX
ASM / Vendor Toolchain
▶
Runtime Loading
JIT Cache
Unified HW Manager

## Slide 9: tle.gpu.local_ptr Design
FlagTree TLE Extension:Shared Memory Pointer Primitive
Core Idea: Introduce dedicated primitives at the Triton language layer so the compiler can recognize shared memory pointer operations and generate specialized instructions
# tle.gpu.local_ptr: Obtain shared memory pointer at a specified position in
def local_ptr(ptr: tl.tensor, offset: tl.tensor) -> tl.tensor:
"""
Returns a pointer to the ( GPU Shared Memory in (ptr + offset) ) location in
and tl.make_block_ptr : directly operates on raw shared memory addresses, enabling the compiler to emit architecture-specific local load/store instructions
"""
Design Points
  Explicitly declare operations on shared memory
  Compiler-visible,lowering pass pass can recognize them
  Under TLE layer provides unified definitions; each chip backend implements local_ptr 's lowering
  Zero runtime overhead

## Slide 10: Compiler Pass Integration
Read from tle.gpu.local_ptr to Architecture-Specialized Instruction Transformation Pipeline
Key Pass:LocalPtrToSharedMemPass
Triton Python
Source Code
FlagGems operator
calls local_ptr
Triton IR
(TTIR)
local_ptr node
preserved in IR
TTGIR
(Triton GPU IR)
Pass identifies
local_ptr node
Specialized Pass
Processing
Replaced with target architecture
local load/store
LLVM IR /
Target Assembly
Generates optimal
memory access instruction sequence
// FlagTree: lib/Dialect/TritonGPU/Transforms/LocalPtrToSharedMem.cpp
class LocalPtrToSharedMemPass : public ...<LocalPtrToSharedMemPass> {
void runOnOperation() override {
// Traverse all tle.gpu.local_ptr operation nodes
getOperation()->walk([&](tle::gpu::LocalPtrOp op) {
// Replace local_ptr with target chip's shared memory intrinsic
rewriter.replaceOpWithNewOp<gpu::SharedMemLoadOp>(op, ...);
});
}
};

## Slide 11: Pass Registration and Backend Integration
Optimization Results
  Reduce global memory round-trip overhead
  Hit shared mem bank locality
  Reduce memory access latency 5~10x
  Improve warp instruction-level parallelism
Pass Registration Pipeline
// Register Pass in backend pipeline Pass
void addPasses(PassManager &pm,
BackendType backend) {
// Common Pass
pm.addPass(createTritonGPUIRPass());
// Specialized Pass (target backend only)
if (backend == BackendType::DCU) {
pm.addPass(
createLocalPtrToSharedMemPass()
);
}
pm.addPass(createLLVMLoweringPass());
}
IR Transformation Example
%ptr = tle.gpu.local_ptr %base,
%offset : !tt.ptr<f32>
%val = tt.load %ptr : f32
// Domestic DCU architecture shared mem access
%ptr = gpu.shared_mem_ptr %base,
%offset
%val = gpu.ds_read_b32 %ptr : i32
Pass ==>

## Slide 12: FlagGems Operator Layer Architecture
How to integrate local_ptr optimization into FlagGems operators
FlagGems — PyTorch ATen Operator Registration Layer
LibEntry / LibTuner — Kernel Cache and Auto-Tuning Management
Triton Kernel — Operator Implementation ( .py ) ← tle.gpu.local_ptr Injection Point
FlagTree Compiler — Specialized Pass Processing local_ptr → Architecture Instructions
Operators optimized with local_ptr (covered in PR #333)
topk
sort
argsort
median
kthvalue
mode

## Slide 13: TopK Operator Optimization Case Study
local_ptr Microarchitecture Optimization in Practice
  Data Proximity Storage: Store intermediate sorting results in shared memory; avoid writing back to global memory and re-reading
  Bank Access Optimization: local_ptr carries offset offset information, enabling the compiler to analyze bank conflict and reorder access patterns
  Instruction Fusion: Pass Replace local_ptr + load into a single ds_read instruction, reducing instruction count
  Latency Hiding: shared memory dispatch latency~5 cycles;warp switching can effectively hide it, significantly improving throughput
# local_ptr optimization: via shared memory
@triton.jit
def topk_kernel_opt(X, OUT_VAL, OUT_IDX,
BLOCK: tl.constexpr):
smem = tl.zeros([BLOCK], dtype=tl.float32)
# Use local_ptr to write to shared mem
ptr = tle.gpu.local_ptr(smem, xidx)
tl.store(ptr, tl.load(X + xidx))
tl.debug_barrier() # for synchronization
# Read from shared mem for sorting
vals = tl.load(tle.gpu.local_ptr(smem, ...))
Optimized: local_ptr Shared Memory

## Slide 14: FlagGems TopK Complete Optimization Path
1
FlagGems Registration Layer
src/flag_gems/ops/topk.py
def topk(input, k, dim=-1, largest=True, sorted=True):
...call Triton kernel...
2
Triton Kernel Layer
Introduce tle.gpu.local_ptr
ptr = tle.gpu.local_ptr(shared_buf, lane_offset)
tl.store(ptr, val) # → shared mem write
3
FlagTree Compilation
LocalPtrToSharedMemPass Processing
tle.gpu.local_ptr → gpu.ds_write_b32
(Domestic DCU shared memory write instruction)
4
Target Code Generation
Architecture-Optimal Instruction Sequence
ds_write_b32 v[addr], v[data]
ds_read_b32 v[out], v[addr]

## Slide 15: Performance Improvement Results
Per-operator performance improvement (relative to pre-optimization, test environment: domestic DCU GPU)
~60%
TopK-class operators Average Improvement
~40%
Sort-class operators Average Improvement
5~10x
shared mem vs. global mem latency ratio
0
Code Intrusiveness (Operator code unchanged)
topk (K=10)
+68%
topk (K=100)
+52%
sort (BitonicSort)
+45%
argsort
+41%
median
+35%
kthvalue
+38%

## Slide 16: Extensibility: Optimization Patterns for Other Op.s
Operator Patterns Suitable for local_ptr Optimization
Intermediate Result Reuse
Operators that read/write the same data multiple times internally
→ Store in shared mem to avoid multiple global accesses
Inter-Warp Communication
Warps within the same CTA need to exchange data
→ Achieve efficient communication via shared mem
Reduction Operations
Cross-thread reductions such as Sum / Max / Min
→ Alternative to traditional shuffle
Block Sorting
Bitonic sort / Radix sort block implementation
→ local_ptr keeps block data in shared mem
Steps to Integrate New Operators with local_ptr
Step 1
Identify shared memory usage scenarios in the operator
Step 2
Replace tl.zeros / tl.full declared shared buffer
to use tle.gpu.local_ptr references instead
Step 3
Verify via FlagTree compilation that the Pass executes correctly
(Inspect the generated PTX / ISA)
Step 4
Verify result correctness in the FlagGems test suite
Step 5
Submit PR; CI/CD automated regression testing

## Slide 17: The Solution: FlagOS, a Unified AI Software Stack

## Slide 18
https://github.com/flagos-ai
https://space.bilibili.com/3546791834290849
https://www.zhihu.com/people/95-22-20-18/posts
https://flagos.io/Home

## Slide 19: Thanks for your time！